## Slide 1
System Spec Goals
 | My LDO | Texas Instruments TLV1171
Minimum Drop Out | 1.0 V | 0.455 V
Required Capacitance | 1 pF | 1 μF
Pos. Settling Time | 10 nano sec | ~ 5 μ sec
Neg. Settling Time | 8 nano sec | ~ 5 μ sec
Pos. Slew Rate | 100 V / μ sec | 5V / μ sec
Neg. Slew Rate | 166 V / μ sec | 5V / μ sec
Quiescent PWR Loss | 2.5 mW | 0.2 mW
Area |  | >> 1.0 mm2
Max. Input | 5.3 Volts | 5.5 Volts
Min. Input | 4.7 Volts | 2 Volts
Max Output Current | 8 mA | 1.0 A
Temperature Range for Vout ±200 mV | 10°C to 45°C | -55°C to 150°C

## Slide 2
First Control System Attempt: PID
KP
+
-
+
+
+
Gate
Drive
Vout
H
Vref

## Slide 3
PID: Great Results, But Too Large

## Slide 4
Reduce to P: Small Enough to Fab

## Slide 5
LDO
Regulator
5.0 Volt VIN
1.3 Volt VREF
GND
VOUT
GND

## Slide 6
Layout Floorplan
VIN RAIL
GND RAIL
VOUT RAIL
OP AMP 1
OP AMP 2
Power
MOSFET
Common
Centroid
Precision
Resistors
250 μm
20 μm
20 μm
200 μm
200 μm
70 μm
0.47 mm
0.29 mm

## Slide 7
Common Centroid Plan
Op Amps
Inverting
Amplifier
Differential
Amplifier
Feedback
Divider
Common centroid
already completed
in homework 4
R1: 1 kΩ
R2: 1.9 kΩ
Unit Resistor
for common
centroid:
0.1 kΩ
R1: 10 kΩ
R2: 10 kΩ
R3: 10 kΩ
R4: 10 kΩ
Unit Resistor
for common
centroid:
5 kΩ
R1: 20 kΩ
R2: 20 kΩ
Unit Resistor
for common
centroid:
10 kΩ