## Slide 1
LDO Regulator
John O’Hollaren

## Slide 2
Standard
Quasi-LDO
LDO
High Dropout
Stability not a problem
Medium Dropout
Stability a concern
Low Dropout
Stability is a big problem
ESR ‘Tunnel of Death’
Linear Regulator Overview

## Slide 3
Black Box I/O Diagram
LDO
Regulator
10 Volt VDD
VIN
-10 Volt VSS
1.3 Volt VBIAS
GND
5 Volt VOUT
GND

## Slide 4
System Spec Goals
 | My LDO | Linear Technology LT1529
Drop Out | 1.1 V | 0.6 V
Required Capacitance | 1 pF | 22 μF
Pos. Settling Time | 2 μS | 150 μS
Neg. Settling Time | 0.1 μS | 100 μS
Quiescent PWR Loss | 1 mW | 0.5 mW
Area | 0.15 mm2 | >> 0.15 mm2
Max. Input (+200 mV) | 8 Volts | 6 Volts
Min. Input (-200 mV) | 12 Volts | 15 Volts
Max Output Current | 0.5 A | 3 A

## Slide 5
First Control System Attempt: PID
KP
+
-
+
+
+
Gate
Drive
Vout
H
Vref

## Slide 6
PID: Great Results, But Too Large

## Slide 7
Reduce to P: Small Enough to Fab

## Slide 8
Steady State Output
Given 10 Volt Input
Easily Produces 5V Output

## Slide 9
4V Sine Wave on Input

## Slide 10
Step Response

## Slide 11
VREF Sweep: Create Many Outputs

## Slide 12
Loop Gain

## Slide 13
Layout Floorplan
VIN RAIL
GND RAIL
VOUT RAIL
OP AMP 1
OP AMP 2
Power
MOSFET
Common
Centroid
Precision
Resistors
250 μm
20 μm
20 μm
200 μm
200 μm
70 μm
0.47 mm
0.29 mm

## Slide 14
Common Centroid Plan
Op Amps
Inverting
Amplifier
Differential
Amplifier
Feedback
Divider
Common centroid
already completed
in homework 4
R1: 50 kΩ
R2: 1 kΩ
Unit Resistor
for common
centroid:
1 kΩ
R1: 10 kΩ
R2: 10 kΩ
R3: 10 kΩ
R4: 10 kΩ
Unit Resistor
for common
centroid:
2.5 kΩ
R1: 1 kΩ
R2: 1 kΩ
Unit Resistor
for common
centroid:
500 Ω

## Slide 15
TODO
(1) Loop Gain
Not very high, I need to figure out how to increase it
This will increase my noise rejection
(2) Power MOSFET Tuning
Currently using a single MOSFET with W/L = 1000
Will experiment with different sizes
(3) Decrease Loop Phase Margin
Faster Response, fairly overdamped currently
(4) Finish Layout

## Slide 16
Thank You